## Slide 1: Data Direct I/O Characterization for Future I/O System Exploration
Mohammad Alian, Yifan Yuan, Jie Zhang, Ren Wang, Myoungsoo Jung, Nam Sung Kim

## Slide 2: The Context of This Paper
Study the data movement between I/O devices and processor/memory in modern servers
System Buses
NIC
SSD

## Slide 3: How did an I/O device traditionally communicate with CPU?

## Slide 4: Example: Traditional Network Packet Reception
2x memory operations for data received from network!
1. device to memory
2. Memory to LLC
3. LLC to private cache and core
NIC
Data

## Slide 5: Example: Traditional Network Packet Transmission
NIC
Optimized for slow I/O and LLC utilization
Buf
1. Fetch network buffers
2. Update network buffers
3. DMA transaction invalidates caches
data
data
4. data copied to device/ written back to memory

## Slide 6: How does a modern I/O device communicate with CPU?

## Slide 7: Example: Network Packet Reception with Intel DDIO
DDIO reduces memory bandwidth utilization
NIC
Data
1. Device to LLC.
2. LLC to private cache and core.
Cacheline in LLC?
✅: Update the cacheline
❌: Allocate a cacheline and write data to that slot

## Slide 8: Example: Network Packet Transmission with Intel DDIO
NIC
1. Network buffer gets updates
Network buffers stay in the LLC for future reference
The network buffer is most likely cached in the cache hierarchy
Buf
Data
Data
2. DMA transaction invalidates private caches
3. Data copied to the NIC

## Slide 9: Experimental Setup
Hardware:
  CPU: Intel Xeon Platinum 8260 x 2
  Memory: 3 channels per socket, 96GB DDR4
  NIC: Intel XL710 40GbE
  SSD: Intel Optane DC P4800X 375GB NVMe
Software:
  DPDK sample applications for networking tests
  FIO micro-benchmark for storage tests
  YCSB + (local) Redis as co-running application

## Slide 10: SSD Read
Memory Read
Memory Write
Memory bandwidth is not a bottleneck in SSD operations

## Slide 11: SSD Write
Memory Read
Memory Write
No LLC invalidation after DMA reads in modern Intel processors

## Slide 12: Network Packet Reception (RX)
Memory Read
Memory Write
Memory bandwidth is not a bottleneck in high bandwidth networking

## Slide 13: Network Packet Transmission (TX)
Memory Read
Memory Write

## Slide 14: Co-running Application
DDIO reduces memory contention in co-running senarios
7.4% performance degradation

## Slide 15: Re-architecting gem5’s I/O Model with DDIO

## Slide 16: gem5
The state-of-the-art architectural simulator
  “The gem5 Simulator: Version 20.0+,” arXive preprint
Comprehensive model library
  Memory and I/O devices
  Full OS, Web browsers
  Clients and servers
Not accurate I/O modeling
  DDIO is not modeled

## Slide 17: Current gem5 model
Components:
  IOBus: noncoherent xbar
  MemBus: coherent xbar
  IO$: small cache sitting between IOBus and MemBus
** IOCache (aka. IO$) is a small cache sitting between IOBus and MemBus
Device
IO$
LLC
MC
DRAM
$
$
C
C
IOBus
MemBus
L2Bus

## Slide 18: Current gem5 model: TX path
Models a DDIO enabled system
  Cores write/allocate in the L1/MLC/LLC
  DMA engine read requests miss in IO$ and are satisfied from LLC/MLC
  IO$ is filled with cachelines in S state
  MLC/LLC copies downgrade into S or O states
Device
IO$
LLC
MC
DRAM
$
$
C
C
IOBus
MemBus
L2Bus
read
miss
snoop
snoop
supply

## Slide 19: Current gem5 model: RX path
DMA writes into IO$
  If wholeCacheline write:
    Send invalidates to CPU side caches
    Write allocate/upgrade in IO$
    The cacheline stays in M state in IO$
  Else: // partial write request
    If miss in IO$:
      Read an exclusive copy of the cacheline
      Update the cacheline with partial write and allocate in M state in IO$
    Else: // hit in IO$
      Send invalidate request to CPU side caches
      Update the cacheline with partial write and upgrade it to M state
Device
IO$
LLC
MC
DRAM
$
$
C
C
IOBus
MemBus
L2Bus
write
miss
inv
inv
snoop
snoop

## Slide 20: Current gem5 model is a Mixture of DDIO Enabled and Disabled System
CPU side caches are invalidated but moved to IO$
DMA engine does not write into LLC
CPU read newly written DMA data from IO$ instead of DRAM
You can have a small IO$ to fairly model an optimized DDIO disabled system
  But not a traditional DDIO disabled system that invalidate caches after DMA reads
Enabled
Disabled
DDIO disabled? DDIO enabled?

## Slide 21: DDIO Modeling in gem5

## Slide 22
Enabled
Disabled
IO$
Enhanced LLC
Device
Device
DDIO disabled optimized: inclusive cache (default)
DDIO disabled: exclusive cache

## Slide 23: Experimental Results

## Slide 24: Methodology
gem5 baremetal full-system mode
  NIC driver that mimics a user-space network software stack (i.e., DPDK)
  RX/TX descriptor size: 1024
Configs
  disabled-op, disabled, enabled
NIC
NIC
gem5 baremetal
1514B packets
40Gbps
2x O3 cores
2.4GHZ
32MB LLC
16ways LLC
DRAM
server
2x DDR4
gem5 baremetal
client
I/O bus
DDIO disabled but DMA reads do not invalidate LLC data
DDIO disabled
DDIO enabled

## Slide 25: Achieved Network Bandwidth
RX
TX

## Slide 26: Packet Reception (RX)
Memory read
Memory write
2 ✕ 1024 ✕ 1514 ≃ 3MB
0.1 ✕ 32MB ≳ 3MB
Only reading headers from the memory

## Slide 27: Packet Transmission (TX)
Memory read
Memory write
No data reuse in our network stack
Lesser conflict with larger LLC
Conflicting writes as ring buffers does not fit in a 2MB LLC

## Slide 28: Summary
Intel DDIO:
  An important technology that facilitates the communication between modern server CPU and high-speed PCIe-based I/O devices.
  We conducted DDIO characterization on a real machine to quantify its benefit.
Implementing DDIO in gem5 simulator
  Download the gem5 patch:
  https://www.dropbox.com/s/5gjpqopu4nlrkx3/ddio-patch.patch?dl=0

## Slide 29: Data Direct I/O Characterization for Future I/O System Exploration
Mohammad Alian, Yifan Yuan, Jie Zhang, Ren Wang, Myoungsoo Jung, Nam Sung Kim