## Slide 1
A Network-Centric Hardware/Algorithm Co-Design to Accelerate Distributed Training of Deep Neural Networks
Youjie Li1, Jongse Park2, Mohammad Alian1, Yifan Yuan1, Zheng Qu3, Peitian Pan4, Ren Wang5, Alexander Schwing1, Hadi Esmaeilzadeh6, Nam Sung Kim1
1UIUC, 2Georgia Tech, 3THU, 4SJTU, 5Intel, 6UCSD

## Slide 2
Training data size (hundreds of TB)
DNN model complexity (hundreds of MB)
Deep learning is growing exponentially!
Training time (weeks or months)

## Slide 3
DNN
Model
Replica
Data
Partition
Worker
Worker
Worker
Worker
Aggregator
Gradient
Weights
Distributed learning is essential!
Parallelizing the learning task over multiple nodes.

## Slide 4
Significant communication overhead in distributed learning!
INCEPTIONN framework
Synchronous training equivalent to TensorFlow
Five Nodes
10 Gb Ethernet
OpenMPI 2.0
Titan Xp GPUs
CUDA 8.0

## Slide 5
Straightforward Solution: Compression
How to reduce communication?

## Slide 6
Challenge #2: Limited compressibility of weights
Train AlexNet with 16-bit FP truncation | Accuracy
Baseline without truncation | 80.2 %
Weight truncation Only | 00.9%
Gradient truncation Only | 79.7%
Challenge #1: Expensive compression overhead
Chart: 
| Communication with 16-bit FP truncation | Original communication time in AlexNet
Communication | 0.5 | 1
Compression | 0.35 | 0
Challenges for compression

## Slide 7
In-network accelerator for compression
INCEPTIONN
Gradient-centric, decentralized training algorithm
Hardware-friendly lossy gradient compression algorithm
A hardware/algorithm co-design to accelerate distributed training

## Slide 8
Pushing the compression to network
General-purpose processors
Conventional practice:
INCEPTIONN:
Heavy overhead
In-network acceleration
Light overhead
FPGAs or
ASICs
Network Interface Card

## Slide 9
Requirements:
High compression ratio
Hardware-friendliness for acceleration
Minimal loss in training accuracy
Solution:
Customized lossy compression algorithm for gradients
Hardware-friendly lossy gradient compression

## Slide 10
High error resilience
Limited range and skewness to zero
AlexNet gradient distribution
Early
Middle
Late
Why gradients?

## Slide 11: Key ideas for lossy gradient compression algorithm
Remove exponents in FP representation by setting it to a constant
Remember the diff by shifting on mantissa with a concat’ed 1
Compress more aggressively as values are close to zeros

## Slide 12
Aggregator
Gradient
Weights
Limitations
Less opportunities for compression
Performance bottleneck at aggregators
Compression with worker-aggregator approach
Worker
Worker
Worker
Worker

## Slide 13
Gradients
Worker
Worker
Worker
Worker
Advantages
Maximize opportunities for compression
Balanced load for compression/decompression
Gradient-centric decentralized training
Approach
Communicate only gradients
Evenly distribute aggregation to the workers

## Slide 14
Implementation

## Slide 15
Name | HDC | AlexNet | ResNet-50 | VGG-16
Model size | 5 MB | 230 MB | 100 MB | 525 MB
Dataset | MNIST | ImageNet |  | 
Mini-batch size | 25 | 64 | 32 | 64
Training data size | 60,000 | 1,281,167 |  | 
System specifications | 
Number of nodes | 4
System software | C++, CUDA 8.0, Intel MKL 2018, and OpenMPI 2.0.2
CPU | Intel Xeon CPU E5-2640 @2.6 GHz
GPU | NVIDIA Titan Xp
FPGA | Xilinx VC709 board
Network | 10 Gb Ethernet
Evaluated DNN models and system specifications

## Slide 16
INC+C offers 76% lower communication time compared to the WA baseline
INC+C offers 2.2~3.1x system-level speedup over the WA baseline
WA: Worker-aggregator
INC: INCEPTIONN
WA+C: WA with compression
INC+C: INC with compression
Training runtime comparison

## Slide 17
Impact on final training accuracy
Only 1 or 2 more epochs are required to match the same level of accuracy

## Slide 18
Conclusion
Gradient-centric, decentralized training algorithm
Lossy gradient compression algorithm
In-network acceleration for compression
INCEPTIONN
Hardware-algorithm co-designed in-network acceleration solution to reduce the communication overhead in distributed DNN training